## Slide 1: ON TO 2050 Development
Chicago Regional Greenhouse Gas Emissions Inventory
Metropolitan Mayor Caucus, Environmental Committee
June 19, 2018
Notes: First talk about process
Then talk about key findings

## Slide 2: Agenda
Project scope
Inventory results
Takeaways
Notes: Notes:
Nature of the memo – more info to come.
Web-based plan means that stakeholders will not access this information linearly.
Expand recommendations to guide development patterns that support reinvestment, fiscal sustainability, economic growth, existing infrastructure, and a strong quality of life

## Slide 3: Greenhouse Gas Emission Inventory Project scope

## Slide 4: Project scope
New inventory for 2015
Updated inventory for 2010
GPC-compliant
7 Counties and the City of Chicago

## Slide 5: Project scope
Contracted with ICF
GPC Basic
Sector | Scope 1 | Scope 2 | Scope 3
Stationary Energy |  |  | NE
Transportation |  |  | NE
Waste |  | NA | 
Industrial Processes and Product Use | NE | NA | NE
Agriculture, Forestry and Other Land Use | NE | NA | NE

## Slide 6: Greenhouse Gas Emission Inventory Results

## Slide 7: Results
2015 Regional Emissions by Sector
Chart: 
| Stationary Energy | Transportation | Waste
 | 0.69 | 0.29 | 0.03
Sector | Total by Scope |  |  | BASIC Total
 | Scope 1 | Scope 2 | Scope 3 | 
Stationary Energy | 32.29 | 49.61 | NE | 81.90
Transportation | 34.13 | 0.35 | NE | 34.48
Waste | 1.42 | NA | 2.01 | 3.43
Total | 67.84 | 49.96 | 2.01 | 119.81

## Slide 8: Results
2015 Total Emissions by County

## Slide 9: Results
Chart: MTCO2e/person
| City of Chicago | Cook (balance) | DuPage | Kane | Kendall | Lake | McHenry | Will
 | 11.5045 | 14.3033 | 14.5747 | 13.649 | 14.209 | 15.591 | 13.8714 | 21.4704
2015 Per Capita Emissions by County

## Slide 10: Results
Chart: 
| Stationary Energy | Transportation | Waste
 | 88.67 | 33.75 | 6.3
2010 Regional Emissions by Sector
Chart: MMTCO2e
| Stationary Energy | Transportation | Waste
2010 | 88.667 | 33.7537 | 6.2973
2015 | 81.902 | 34.0696 | 3.1585
2010-2015 comparison

## Slide 11: Results
Chart: MMTCO2e
| 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Estimate | 128.7181 | 119.1302
Scenario 1 | 119.1302 | 125.3563 | 130.1586 | 134.6591 | 139.0372 | 143.2314 | 147.1974 | 151.2907
Scenario 2 | 119.1302 | 114.7493 | 109.0636 | 103.2872 | 97.6215 | 92.0569 | 86.6007 | 81.4774
Scenario 3 | 119.1302 | 104.1422 | 89.8325 | 77.2105 | 66.2296 | 56.6813 | 48.3929 | 41.3213
Climate Stabilization Goal | 24.7911 | 24.7911 | 24.7911 | 24.7911 | 24.7911 | 24.7911 | 24.7911 | 24.7911 | 24.7911
2015 Per Capita Emissions by County

## Slide 12: Greenhouse Gas Emission Inventory Takeaways

## Slide 13: Takeaways
Start the data collection as early as possible
  Especially for utilities
Significant sources of emissions are not included at the GPC Basic level
  The report is likely undercounting emissions
Consider GPC Basic+ for smaller areas
Notes: Notes:
Nature of the memo – more info to come.
Web-based plan means that stakeholders will not access this information linearly.
Expand recommendations to guide development patterns that support reinvestment, fiscal sustainability, economic growth, existing infrastructure, and a strong quality of life

## Slide 14
Thank you!
Jared Patton jpatton@cmap.Illinois.gov