## Slide 1: Warm-Mix Asphalt
An Opportunity for Environmental Protection
Presented by Edith Makra - Metropolitan Mayors Caucus
Prepared by US EPA
January 22, 2019
Presentation Courtesy of:

## Slide 2: Warm Mix Asphalt
Air quality issue
Potential for environmental benefits
EPA seeking to promote WMA
Sustainability opportunity for municipalities
MMC seeking recommendation from public works

## Slide 3: Emissions from HMA facilities
EPA Assessed Hot Mix Asphalt impacts
reports https://www3.epa.gov/ttnchie1/ap42/ch11/related/c11s01.html

## Slide 4: What is Warm-Mix Asphalt?
Hot-Mix Asphalt (HMA)
  94% of all roads
  Asphalt Binder + Aggregate
  300°F - ~350°F
Warm-Mix Asphalt (WMA)
  Binder + Aggregate + Additive
  270°F - 300°F

## Slide 5: How is Warm-Mix so cool?
Reduced Viscosity
  Aggregate coated easier at lower temperatures
3 methods:
  Water injection (foaming)
  Organic Additives (waxes)
  Chemical Additives

## Slide 6: Economic Benefits
Lowering temperatures reduces fuel use by 20%-35%
Increased Production
Shorter project timelines
Longer hauls
Increased use of Reclaimed Asphalt Pavement
Cold-weather paving

## Slide 7: Performance Benefits
Compaction Aid
  Improved in-place density
  Better Durability – every 1% = 10% increase in pavement life
Decreased Plant Wear
Improved temperature uniformity
Longer placement window
Increased workability

## Slide 8: Environmental Benefits WMA vs HMA
Reduces Air Pollution & GHGs:
  VOCs – 50%
  NOx – 60%-70%
  SO2 – 30%-40%
  CO – 10%-30%
  PM – 20%-25%
  CO2 – 30%-40%
Reduces Odors & Fumes
Improved Conditions for Workers
LEED Credits

## Slide 9: Benefit Quantification
Illinois:
200+ Asphalt Plants
14 million tons of asphalt in 2016
CO2: 69,300 tons
    13,400+ Cars
    2,000,000+ LEDs
    74,000+ Acres

## Slide 10: Benefit Quantification
Highland Park:
7500 tons/year
  VOCs: 0.03 tons
  NOx: 0.06 tons
  SO2: 0.004 tons
  CO: 0.05 tons
  PM: 0.025 tons
  CO2: 37.00 tons
    7 Cars
    1100 LEDs
    40 Acres
Contractor:
136,000 tons/year
  VOCs: 0.6 tons
  NOx: 1.1 tons
  SO2: 0.23 tons
  CO: 1.0 ton
  PM: 0.5 tons
  CO2: 673 tons
    131 Cars
    20,000 LEDs
    720 Acres

## Slide 11: Sustainability Opportunity for Municipalities

## Slide 12: Boost Demand

## Slide 13: Sustainable Paving
• Reduce the energy and emissions associated with mixture production by adopting WMA technologies.

## Slide 14: Obstacles
Specifications
Contract bids
Initial investment
Lack of supply
Lack of demand
Lack of awareness
Longevity & performance fears

## Slide 15: Potential for Municipal Use of WMA
WMA not widely used by municipalities
Asphalt widely used by municipalities
Need guidance & specs
Peer learning
Capture and report environmental benefits

## Slide 16
Thank you:
Alexis Cain
312-886-7018
cain.alexis@epa.gov